## Slide 1
Group by :-
K. Chandrakala
N. Keerthi
V. Ayyappa Reddy
V.L. Bhanu Prakash Reddy
GUIDED BY :-
Mr.N. SREERAMULA REDDY
ASSISTANT PROFESOR
Electrical and Electronics Engineering
Annamacharya Institute of Technology and Sciences, AUTONOMOUS :: Rajampet
Project Review
A Presentation
On
“ Design and development of automated writing machine”
DEPARTMENT OF ELECTRICAL AND ELECTRONICS ENGINEERING

## Slide 2
Contents:-
      Introduction
      Objective
      Existing System
      Proposed method
      Tools Required
      Working
      Software Working
      Future Plan

## Slide 3
We have the technologies like printers, scanners, etc. But the basic problem is it only
writes only those fonts which the computer already has. That is Roman, Calibri, Arial,
Impact, Georgia, etc. We want a machine which can write the full matter on a page by
the ink of pen in our own personal hand writing. By using the concepts like CNC
machines which make easy to scan the text. Similarly, we can use this technology
to make a machine for Writing purpose, but also used for Drawing purpose.
INTRODUCTION

## Slide 4: Objectives
The machine can be used for writing by giving the input to the machine.
This machine can able to write the text and drawing the diagrams, just like hand written notes and drawings.
The automated writing machine is used to save our time.

## Slide 5
Existing System
The already existing technologies like printers, scanners is that they only write in predefined fonts present in the computer.
The proposed system works as an automated writing machine that is capable of Writing in any predefined font or in the user's hand writing style.

## Slide 6
Text Identification
Font converter
OUTPUT
WRITE – UP COPY
Block Diagram
INPUT
Text
Proposed Method :-

## Slide 7
Hard ware :-
  Stepper Motor
  Servo Motor
  Rods
Tools Required

## Slide 8
Stepper Motor:
These are electromagnetic devices that convert digital pulses into mechanical shaft rotation in discrete steps. These motors provide high accuracy, low cost, high torque, high reliability, and simplicity to the system. In the proposed system stepper motors like Nema 17 are used to achieve motion in the x and y-axis.
Step angle | 1.8 degrees
Current | 1.2 A/Phase
Holding Torque | 4.2 Kg-Cm
Detent Torque | 2.2N.Cm
Lead Wire | 4
Shaft Diameter | 5mm
Specifications:

## Slide 9
Servo Motor:
Servo motors are special electromagnetic devices that produce precise degrees of rotation. Servo motors work on the principle of pulse width modulation, where the applied pulse duration given to the control pin controls the motor’s rotation angle.
Weight | 55gm
Dimensions | 39.5mm*20.5mm*40.7mm
Operating Voltage | 4.8 ~ 6.6 V
Gear type | Metal Gear
Temperature range | 0- 55 Deg
Servo wire length | 30 Cms
Speed | 3000 – 5000 rpm
Operating Speed | 0.20 sec / 60 Degrees (4.8 V)
Specifications:

## Slide 10
Linear Rods:
Long, thin, straight metal bars known as linear rods are frequently utilized in a variety of applications that call for load-bearing or structural support.
1. Robotics: Precision linear motion in the X, Y, and Z axes is provided by linear rods in robotics applications.
2. Manufacturing: In order to support numerous components, including convey or systems, assembly lines, and machining equipment, linear rods are employed in manufacturing processes.
Diameter | 12mm
Length | 450mm
Tolerance | -0.005mm to -0.03mm
Specifications: Linear Rod - 450mm
Diameter | 8mm
Length | 350mm
Tolerance | -0.005mm to -0.03mm
Linear Rod - 350mm
Specifications:

## Slide 11
Software
Arduino:- Arduino is an open-source electronics platform based on easy-to-use hardware and software. Arduino boards can read inputs – light on the sensor, and turn it into an output – activating a motor, turning on an LED, publishing something online.

## Slide 12
Inkscape 0.9.2
To create the plotted figure or text, use Inkscape. With this software, a G-code file of a chosen image or piece of text is made for this project. X, Y, and Z coordinates are part of the widely used numerical control programming language known as G-code..

## Slide 13
G – CODER: -
"G" is presenting this. G-codes are pre-defining functions linked to Machine Axis Movement. It is a two-digit number, such as G00, G81, or G90. It is possible to place multiple G addresses in a single block. As long as these Functions do not conflict with one another. G02 and G03, which are located together in a single block, are not permitted. The path that must be taken to create a whole design is specified by the g function. positioning with
ExG00- positioning.
G01- Linear interpolation
G02- Clockwise Circular Interpolation
G03- Counter clockwise Circular Interpolation G04- Dwell

## Slide 14
WORKING
Install the inkscape, UGS, 4XIDraw Tool software in system.
The programming code will be uploaded in the Arduino uno board once the devices is fixed.
The sensors used recognize the user input and fetch user input with stored document and return results and start writing on paper.

## Slide 15
Step 1: Install Inkscape software 0.9.2
Software Working

## Slide 16
Step 2: Open the Inkscape application

## Slide 17
Step 3: After that we can take text option and text

## Slide 18
Step 4: We will go to the extension file and we can select “KM laser” in that file.in
KM laser we can select “convert Hershey text” (for converting text into different fonts)

## Slide 20
Step 5: After that font has been applied then it is converted in a selected font.

## Slide 21
Step 6: We will go to the extension file to select “4xdraw tools” again and select “generate pen GCODE tool”.

## Slide 22
Step 7: We can select pen movement (up and down) travelling speed, servo angles and delay time.In dictionary we can select file location after we can give file name and click on the “apply” option

## Slide 23
Step 8: Next open UGP (universal Gcode platform) version 2.0.12. we can connect Arduino connection whether it is Connect or not.

## Slide 24
Step 9: Click on the connect or disconnect option. It is connected open file we can select file already which is saved in the inkscape.

## Slide 25
Step10: After that we can select the file and open it. The automatically the source will display

## Slide 26
Step 11: In control state (DRO). We can set x-axis, y-axis and z-axis are zero. after we can run it.Before starting the pen movement in console we have to give
commands for pen up and down.
Pen up=M03 S80
Pen down=M05 S10

## Slide 27
Step 12: After that it shows the pen movement how much speed it goes on x, y, and z-axis.

## Slide 29
WORKING MECHANISM
Text Text Font Detection Extraction Conversion
GCode
Image Generated
User Interface Terminal Software
Ardunio Board
Gantry setup
Power supply
Stepper Motor
Servo motor
Pen movement
Input document / text writing
Software
Hardware

## Slide 30
Results
Amazon, the multinational e-commerce grant, has done the impassible and reached a staggering 18 Trillion dillars market cap in the past few years, and is expected to reach over 18 Trillion in revenues by the year 2025.
INPUT
OUTPUT

## Slide 31
Input image
Output image

## Slide 32: FUTURE PLAN
The proposed system can be used as a baseline setup for many future modifications
  Increase the speed of writing compared to the speed achieved currently.
  Inclusion of voice-to-text modules in the already proposed system, which will be beneficial for differently abled people.
  The system can be extended to read doctor’s prescriptions which in turn can be converted to the user’s language using a language translation model.

## Slide 33
THANK YOU…